## Slide 1: C-space and RRTs
Dr. Troi Williams
Slide Credits: Pratap Tokekar

## Slide 2: Note
Extra Lab days on Tuesday, March 10th and Thursday, March 12th.

## Slide 3: Configuration
A configuration is a complete specification of every point of the robot
C-space is the space of all possible configurations
Some examples:
  a point robot that can translate in 2D:
  a robot that can rotate and translate:
  a two link manipulator:

## Slide 4: Solution v2
Randomly pick a sample configuration, xi
Check if qi is collision-free
If qi is in Cfree then add it to the graph
  add edges to existing vertices (more details later)
If qi is not in Cfree, then discard it
Check if we have found a path, else repeat

## Slide 5: Rapidly Exploring Dense Trees (RDTs)
One of the most popular techniques
Introduced by LaValle in ‘98
  many, many, many extensions and variants
http://planning.cs.uiuc.edu
Ch 5.5, 5.6, 14.4

## Slide 6: RDTs vs RRTs vs PRMs
Many versions of the same idea
  with different guarantees
Rapidly exploring Random Trees
  randomly sample the C-space
  graph built will be a tree
Rapidly exploring Dense Trees
  any sequence of samples (not necessarily random)
Probabilistic Roadmaps
  build a general graph (roadmap) instead of a tree
  useful for multiple queries with diff. start and goals

## Slide 7: And many, many variants
articulated robots
kinematics, dynamics, differential constraints
http://msl.cs.uiuc.edu/rrt/gallery.html (circa 2000)

## Slide 8
starting configuration
sampled config.
nearest point on the tree

## Slide 9
assume no obstacles
if nearest point lies on an existing edge, then split that edge

## Slide 10
recall that there is no parameter involved

## Slide 12: What about the goal?
So far, RDT is only building a tree
Occasionally add the goal configuration and see if it gets connected to the tree
  say every 100th iteration

## Slide 13: Remember
We are in the C-space
A vertex in the graph is a specific configuration
How to find the nearest configuration?
  What is the distance function?

## Slide 14: Distances in C-space
The C-space is not necessarily Euclidean space
Need to define appropriate distances
  e.g., distance along a circle for 1-link manipulator
  e.g., distance along the surface of the torus for a 2-link manipulator

## Slide 15: Distances in C-space
The C-space is not necessarily Euclidean space
Need to define appropriate distances
Each edge represents a path in C-space
  An edge means that there is a collision-free path between two configurations

## Slide 16: Practical Solutions
Use a step size parameter
Move in steps and check collision of a configuration
Often, a local steering function is used instead*
* more details later
https://personalrobotics.ri.cmu.edu/files/courses/papers/Kuffner00-rrtconnect.pdf

## Slide 17: Tree “grows” from the start config. due to step size parameter
without step size
with step size
Notes: with

## Slide 18: Demo
run_rrt.py
  Change DELTA and observe the effect on the running time and path length

## Slide 19: Guarantees?
Is RRT complete?
  No but it is probabilistically complete – if there exists a path, the probability that RRT will not find the path decays to zero as the number of samples approaches infinity.
Is RRT optimal? No
  “… the probability that the RRT converges to an optimum solution, as the number of samples approaches infinity, is zero under some reasonable technical assumptions.”
  RRT* is optimal

## Slide 20: RRT*
https://arxiv.org/pdf/1005.0416.pdf
TL;DR: Samples a point, try to connect it to the tree via the Extend function, then repeat.
Result: a tree that incrementally approximates the reachable space.
TL;DR: (Vanilla RRT extension–it is not optimal).
Adds a new node to the graph if the node is collision-free.

## Slide 21: RRT*
https://arxiv.org/pdf/1005.0416.pdf
TL;DR: RRT extension that rewires for optimality.
First Loop: Picks the cheapest way to insert the new node.
Second Loop: See if the new node can make any of its neighbors cheaper and rewire them.
Same steps as before.

## Slide 22: RRT*
https://arxiv.org/pdf/1005.0416.pdf

## Slide 23: Why are RRTs so popular?
Once you define the C-space and implement following subroutines, the actual algorithm is very simple:
  random configuration generator
  nearest neighbor
  collision checker
In practice, it works rather well.
Can add heuristics on top, e.g., bias the random config. generator towards goal configuration

## Slide 24: EXTEND() is the real crux
EXTEND() takes the tree and extends it closer to the given random configuration
We saw the Euclidean case where the extension is a straight line
In general, kinematic (and dynamic) constraints can be handled within EXTEND()

## Slide 25: Example: car-like robot
Configuration is ??

## Slide 26: Example: car-like robot
Configuration is (x,y,𝜽)
Robot can’t slide sideways
  Suppose q = (0,0,90°) and qnear = (1,0,90°)
  Can we draw an edge?
Solving for a feasible path from q to qnear is as hard as the original problem

## Slide 27: Example: car-like robot
Solving for a feasible path from q to qnear is as hard as the original problem
Does not matter
Just apply a random or best control input for a fixed time to obtain qnew in NEW_CONFIG()

## Slide 28: Practical Matters
Configuration space
  OMPL: ompl.kavrakilab.org/
Nearest neighbor search in high dimensions
  FLANN: https://www.cs.ubc.ca/research/flann/
Collision Checking
  FCL: https://github.com/flexible-collision-library/fcl
Integration with sensors and ROS
  MoveIt! https://moveit.ros.org

## Slide 29: Try it out
Install OMPL.app on your machine
https://www.youtube.com/watch?v=EsXM4VLWxkE

## Slide 30: Configuration space (OMPL)
Most commonly used ones are already defined
2D/3D rotations
2D/3D translation + rotation
Car-like robots

## Slide 31: Combine spaces
For example, to get the state space of a manipulator arm one could combine R5 and SO2 (circle) to represent 5 joints that have bounds and one joint that can rotate continuously
*OMPL calls configuration space as state space

## Slide 32: Distance function
To compute nearest neighbors using FLANN
Already implemented for common spaces

## Slide 33: Collision Checking
OMPL doesn’t do collision checking
Instead, you can choose to use any existing collision checker --- commonly used one is FCL

## Slide 34: Collision Checking – FCL
Normally, instead of using FCL directly, you should use it through ROS (with the MoveIt! Package)

## Slide 35: Collision checking – MoveIt!